## Slide 1
Lesson 10
Airspace

## Slide 2
Key References
https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/phak/media/17_phak_ch15.pdf
https://www.faa.gov/air_traffic/publications/media/aim_bsc_w_chg_1_2_dtd_5-19-22.pdf

## Slide 3: Overview & Objectives
Understand the U.S. National Airspace System
Be able to list and define all classes of U.S. airspace
Know VFR weather (visibility and cloud clearance), equipment, and ATC clearance requirements for each airspace
Be able to determine from a sectional map, what airspace a pilot is in at any point/altitude
Know sources for airspace study including Skyvector.com, the AIM, (and FARs Part 91 which is a later lesson)
Lesson Review & Summary
Questions
Quiz

## Slide 4: Key Airspace Discussion
Airspaces are designated to support VFR, IFR, Military Training, GA, Airlines, etc.
Controlled airspace includes: A, B, C, D, E airspaces (maps/graphics later)
A = High ‘Altitude’ (18,000’ MSL/FL180 up to FL600) … IFR flight only
Airports w/ ATC control are B (‘Big & Busy’), C (‘Continuous Ops’), D (‘Daytime Tower’)
Key airspaces for VFR pilots for local training and XC are E and G
  E is controlled airspace (read as ‘controllable’) airspace from 1201’ AGL to 17,999’ MSL (E varies)
  G is ‘UNCONTROLLED’ airspace surface to 1200’ AGL (G also varies … more to follow)
Military Operations Areas: VFR military training (e.g., “Eagle MOA”)
  Legal for VFR pilot to fly in with extremes caution if active … magenta hashed areas ///////
Restricted Areas: Military Weapons Ranges (e.g., “R-5303A”)
  Pilots may not fly through restricted areas w/o ATC Clearance … blue hashed areas ///////
Prohibited Areas: Is what it says…don’t go there (e.g., “P-79”) … heavily marked/obvious
National Parks and Wildlife Refuges (“Buffalo Wildlife Refuge”) … dotted/circled/blue
  No fly < 2,000’ AGL

## Slide 5: ATC ‘Center’ Boundaries (reference only)
We can use ATC Center or Regional Approach Controllers for ‘flight following’ during cross-country flights

## Slide 6: Airspace Aquarium

## Slide 7
A
C
D
E
B
G
Airspace Table (Equipment/Entry/VFR Weather Requirements) - CRITICAL
Airspace
Distance from Clouds
Visibility
Must be IFR …
Comm, Transponder w/Mode C, ADS-B, (+ ‘Clearance’ to Enter)
Comm, Transponder w/Mode C, ADS-B (must call approach prior to entry but clearance to enter WILL be granted)
Comm (must call tower prior to entry but clearance to enter WILL be granted)
No Comm/Transponder/ADS-B Req’d
Equip & Entry Requirements (indicated if clnc/approval required)
No Xpndr or ADS-B Req’d
Xpndr w/Mode C & ADS-B Req’d
Comm NOT required in Class E Hi/Lo

## Slide 8: Combined Airspace Info & Aquarium
3-152
COMM
3-152
3-CLR
XPNDR
COMM
ADS-B
CLNC
3-152
COMM
XPNDR
ADS-B
5-111
Day 1-CLR
(Night 3-152)
3-152
Class A – IFR only – ‘Flight Levels’
(altimeter set to 29.92)
Class E
‘E Hi’ = 10K-17,999’MSL,
‘E Lo’ = <10K MSL)
VFR or IFR
(use local altimeter)
5-111
Day 1-152 (Night 3-152)
5-111
Day 1-152 (Night 3-152)
5-111

## Slide 9: Relating the Airspace Aquarium to the Sectional Map
On the following slides, we will look at several examples of airspace on sectional map excerpts.

## Slide 10: Identifying Airspaces on a Sectional Map
Class E Surface Area
Class D
- Solid lines generally identify full-time controlled airspaces (most airspace is full-time/does not change)
Dashed Line means part-time…call it “Dashed for Day only” (only Class D and Class E Surface areas)
Soft fat lines means that the airspace does not reach the surface (this is the “E Dip”)
Class E
Class E
Class E

## Slide 11: Identifying Airspaces (cont)
Class C
Class E
Class D
Class D
Class D
Class E
Note ‘Victor’ Airways (e.g., V-63 below) … pilots may file VFR flight plans on those routes
Wildlife Area

## Slide 12: Identifying Airspaces (cont)
Class D
MOA
Class E
Class E
Class E
Class E
RESTRICTED AREAS
MOA
MOA

## Slide 13: Identifying Airspaces (cont)
Class B
30 NM ‘Mode C’ line
Class D
Class D
Class D
Class E
Class E
Class E
Class E
Class E

## Slide 14: Identifying Airspaces (cont)
Identifying Airspaces (cont)
PROHIBITED AREA

## Slide 15: On-line Airspace Review http://www.skyvector.com/
Example here is KXNA, a Class C airport in NW AR with multiple Class D and various uncontrolled fields surrounding. Recommend instructors/students use the ‘World VFR’ (or e.g., Kansas City) ‘Sectional’ map button at the top right, to step through multiple examples of Class B, C, D, E-Surface, and G airports/airspaces around the nation. Discussion: Note how this newer airspace was designed with a wide encompassing Class E ‘dip’ around the controlled airports.

## Slide 16: Review & Summary
Understand the U.S. National Airspace System
Be able to list and define all classes of U.S. airspace
Know VFR weather (visibility and cloud clearance), equipment, and ATC clearance requirements for each airspace
Be able to determine from a sectional map, what airspace a pilot is in at any point/altitude
Know sources for airspace study including Skyvector.com, The AIM, (and FARs Part 91, which is a later lesson)
Quiz to follow…

## Slide 17
Next Up: Navigation & Flight Planning
Ref: PHAK Chapter 16 & Skyvector.com
Questions?